## Slide 1: Comfort Flexibility Service
Energy data
Input indoor & environmental
data
Grid requests
Comfort model
Comfort-based flexibility outcomes
Optimal trade-off solution between comfort & energy
Optimization algorithm
Comfort flexibility model
Building level
Decision phase
Building level
Comfort Flexibility Service
Objective:
Develop a human-centric demand response service that prioritizes people comfort while enhancing building energy performance through personalized comfort flexibility actions for the next day.
The service will propose to the building manager three different solutions for the next day:
Optimal comfort minimizing energy consumption
Acceptable comfort minimizing energy consumption
Minimization of energy consumption without prioritizing comfort
Each solution always guarantees comfort.
Notes: Spiegazione del servizio in generale:
The proposed service consist in a human-centric demand response service that prioritizes people comfort while enhancing building energy performance through personalized comfort flexibility actions for the next day.
This approach is structured around three main components, as shown in Figure.
The first component is the Building Level, which involves the collection of data through sensors installed in the apartment or building under analysis. These sensors provide real-time information about the indoor environment, forming the basis for the next block.
Next is the Comfort Flexibility Model. In this block, the data collected is analyzed to assess people comfort (comfort model) and to provide comfort flexibility reccomendations for the next day (optimization algorithm). If you want Diego you can also list the three different solutions as reported into the slide.
Finally, we reach the Decision Phase, where the insights gained from the flexibility model are combined with grid request. This phase leads to a decision that aims to obtain the optimal trade-off between comfort, energy efficiency and building performance.

## Slide 2: Comfort Flexibility Service
In this service, AI plays a key role, particularly in predicting two fundamental parameters:
Energy consumption/production
provided by an external partner involved in the Dedalus project.
Thermal comfort
assess through Thermal Sensation Vote (TSV).
Initially, a machine learning model is trained to associate the TSV with internal environmental conditions and user feedback (TSV). Once trained, the model can predict the TSV for the following day based solely on historical data.
Then the optimization model is applied (Pareto efficiency-based approach) which generates three alternative recommendations. Each of these ensure user comfort during DR events.
LSTM+ML
Energy forecasted for the next day
Optimization
algorithm
Comfort-based flexibility reccomendations for the next day
Historical dataset
Tout,Tin,RH,CO2, hour, day of the week, is_weekend
Tin predicted
RH predicted
LSTM layers:
1 layer 64 units, dropout 0.2
2 layer 32 units,dropout 0.2
Dense 16 units, ReLU
Dense 1 unit, linear
Optimizer: Adam learnig rate 0.001
TSV predicted
AI BLOCK
Notes: Spiegazione del workflow schematizzato:
Starting from historical data, AI is used to obtain the comfort flexibility recommendations. This AI approach is a combination of LSTM and ML techniques, and it is employed to predict both the internal parameters expected for the following day and the Thermal Sensation Vote (TSV). Subsequently, the predicted TSV and the energy forecast for the next day are used in the optimization block to generate the three possible solutions, as previously explained.